NORDANE SHIPPING A/S

Kullinggade 31 C, DK 5700 Svendborg, Denmark.

Telephone  +45 62 22 27 77,  E-mail info@nordane.dk

Tug     M/V "STEVNS MASTER"

Built by H. H. Bodewes Shipyard Millingen Holland  1971.

Call sign 0ZTB 2.  IMO No. 7116858     GSM +45 23 34 72 75.

Length overall:  	31,50 m.

Length betw. p.p.: 	28,00 m.

Breadth moulded:	8,75 m.

Breadth extreme:	9,15 m.

Depth moulded:	5,00 m.

Draft midship u.s. keel:	3,95 m.

Gross tonnage:                       282.

Nett tonnage:                            84.

Speed max:                       13,5 kn.

Max range:                          Nav.m.

Class:  Germanischer Lloyd + 100 A 5

Tug, E 1 MC E 1.

Trading area:  World wide within sea area A 1 and A 2.

Main engine:  Deutz 6M358 1470 kW.

1 fixed propeller in steering nozzles.

Auxiliary machinery:

2 x 140 kVA  3 x 380 V.
1 x   70 kVA  3 x 380 V.
Bowthruster:  184 kW.

Towing equipment etc:

Certified bollard pull:   	30 t.

Towing hook

Navigation equipment etc.:

Radar 1: Racal Decca BT 501

Radar 2: Furuno 1932.

Radar 3: Furuno 821.

DGPS Navigator: Furuno GP 30.

VHF 1: Debeg 7606.

VHF 2: Debeg 7619.

VHF 3: Sailor RT 2048.

Autopilot: Robertson AP 45.

Fire fighting equipment:

One pump set of 180 cbm/14 bar, two pump

Combine 220 cbm/hrs/5bar, 110 cbm/10bar

3 monitor for water/foam. One hyd./snorkel type 22m above water 180cbm + two fixed 9 m above water each. 60 cbm. Foam 27 cbm storage.

Accommodation for 6 persons.